## Slide 1: Assessment of thermospheric models in NASA/CCMC ecosystem
Jack WANG, Jia YUE
CCMC, NASA GSFC, USA
Catholic University of America, USA
Richard MULLINI, Chiu WIEGAND, Masha M. KUZNETSOVA,
M. Leila MAYS,
CCMC, NASA GSFC
Sean BRUINSMA
Centre National D’Etudes Spatiales, France

## Slide 2: Aerodynamic Drag in the Thermosphere = Space Object Positioning Error
Expected position
Actual position
drag force
neutral density
The major source of uncertainty in determining the precise orbital location of objects
in Low Earth Orbit is the computation of the acceleration due to atmospheric drag

## Slide 3: COSPAR ISWAT initiative: Thermosphere model assessment under storm conditions
Operationally-relevant metrics for modeled neutral density under storm conditions have been developed (Bruinsma+, 2021).
Assessment during 13 storms was done for semi-empirical models (NRLMSISE-00, JB2008, DTM2013, DTM2020), and physics-based thermosphere-ionosphere models (TIE-GCM, CTIPe).
Achievements
International Space Weather Action Team G2A
http://www.iswat-cospar.org

## Slide 4: Thermosphere model assessment: dataset & CCMC involvement
Runs-on-Request
Kamodo
CAMEL
community challenges/campaigns
Simulation
Analysis
Validation
High-fidelity thermosphere density data download from the CHAMP, GRACE, GRACE-FO, GOCE, and Swarm missions @ ftp://thermosphere.tudelft.nl
Reformatted observation dataset is publicly accessible
@ https://git.smce.nasa.gov/ccmc-share/camel-data

## Slide 5: Thermosphere model assessment: CCMC involvement Ⅰ
In the current project, multiple unique time periods during storm times are selected for the assessment.
In addition to the aforementioned models, NRLMSIS 2.0, GITM, WACCM-X were run in-house at CCMC Runs-on-Request system and accessed.
Runs-on-Request (ROR) is a free service open to any user interested in running the space science/space weather models hosted at the CCMC. Simulation output can also be directly downloaded at result pages.
NRLMSIS 2.0
JB2008
GITM
TIE-GCM
CTIPe
DTM2013
WACCM-X
CCMC Model Catalog
semi-empirical
physics-based thermosphere
physics-based whole atm.
WAM-IPE
DTM2020

## Slide 6: Thermosphere model assessment: CCMC involvement Ⅱ
The CCMC-hosted physics-based model flythrough is conducted by
Simplify validation workflow.
Kamodo is a Python open-source software package developed by the CCMC, which offers a model-agnostic satellite flythrough capability.
Kamodo GitHub repo
Simulation Output

## Slide 7: Thermosphere model assessment: CCMC involvement Ⅲ
The neutral density validation project is built upon the CAMEL (Comprehensive Assessment of Models and Events Using Library Tools) framework developed and hosted by the NASA CCMC.
https://webserver1.ccmc.gsfc.nasa.gov/camel/NeutralDensity/

## Slide 8: CAMEL Neutral Density Validation: Definition of storm phase

## Slide 9: CAMEL Neutral Density Validation: Definition of storm phase
pre-storm
main
recovery
post-storm
36 hours
18 hours
Dst min
debias
metrics (Bruinsma+, 2021):
  mean normalized (debiased) O/C ratio
  standard deviation
O: observation
C: computed (model solution)
storm phase

## Slide 10: CAMEL Neutral Density Validation: Single Event Data Plots
parameter | Density, Normalized density, Observed-to-Computed (O/C) ratio, Normalized O/C ratio

## Slide 11: CAMEL Neutral Density Validation: Skillscore - Mean of Normalized Density Ratio
NRLMSIS 2.0
CTIPe
DTM2013
DTM2020
intermediate
DTM2020
operational
GITM
JB2008
TIE-GCM
WACCM-X
skills by phase
1.129
1.116
1.141
1.297
1.279
1.316
0.984
0.983
0.986
1.023
1.045
1.001
1.059
1.071
1.048
1.190
1.210
1.033
1.023
1.042
1.018
1.094
0.943
1.099
1.116
1.083
main phase
recovery phase
average
>1 underestimated
1 = best score
<1 overestimated
1.171

## Slide 12: Future outlook: unify drivers for model assessment
Initial Condition Dominated
Forcing Dominated
weather
thermosphere/
ionosphere
magnetosphere

## Slide 13: Future outlook: unify drivers for model assessment
Initial Condition Dominated
Forcing Dominated
weather
thermosphere/
ionosphere
magnetosphere
high-latitude
electric potential models
particle precipitation
models
solar irradiance
models
thermosphere/ionosphere models: CTIPe, TIE-GCM, GITM
lower atmosphere
models
lower atmosphere
observations
whole atmosphere models:
WACCM-X, WAM-IPE
Driver from below
Driver from above

## Slide 14
CCMC CAMEL tool ensures transparency, inclusion, and community involvement in the validation studies.
model developers
Simulation
Notes: The CCMC CAMEL tool ensures the transparency, inclusion, and collaboration in validation studies.

## Slide 15: Summary
NASA CCMC, as a participant of the COSPAR ISWAT action team G2A, has built and hosted the interactive neutral density validation web tool upon CAMEL framework, with community involvement and coordination.
A follow-on study will upload quiet-time model datasets into CAMEL, and validated against the measurement by satellites.
The CAMEL front-end will also be upgraded after feedback from the community are received.
Notes: The CCMC CAMEL tool ensures the transparency, inclusion, and collaboration in validation studies.